## Slide 1: Introduction to 3GPP Release 19 and 6G Planning
Wanshi Chen (Qualcomm, Chair of 3GPP RAN Plenary)
Puneet Jain (Intel, Chair of 3GPP System Architecture)
Moderated by Iain Sharp (ATIS, Principal Technologist)
April 3, 2024

## Slide 2: Agenda
Wanshi Chen Qualcomm 3GPP RAN Plenary Chair
Iain Sharp
ATIS
Puneet Jain Intel Corporation 3GPP SA Plenary Chair
Introduction
Q&A
3GPP RAN: Current Status and Beyond
3GPP SA Release 19 Status Update and 6G Planning

## Slide 3: 3GPP RAN: Current Status and Beyond
Wanshi Chen
3GPP TSG RAN Chair
Sr. Director, Technology, Qualcomm Technologies, Inc.

## Slide 4: Outline
Overview
3GPP RAN Release 18 (Rel-18)
3GPP RAN Rel-19
Initial 6G Discussion

## Slide 5: Overview

## Slide 6: 5G and 5G-Advanced in 3GPP
Rel-16 Industry Expansion
Rel-17 Continued Expansion
Rel-15 eMBB Focus
5G-Advanced: Rel-18, 19, …
eURLLC and TSN for IIoT
NR in unlicensed
5G V2X sidelink
Multicast
Lower complexity RedCap
Non-terrestrial communication (satellites)
Unlicensed/licensed spectrum in 60 GHz
Improved IIoT, positioning V2X, IAB, …
5G NR foundation
Smartphones, FWA, PC
Expanding to venues, enterprises
Next set of 5G releases (i.e., 18, 19, 20, …)
Rel-18 work completed in Dec’2023
Rel-19 work started from 1Q’2024
In-band eMTC/NB-IoT
Positioning
2nd wave of 5G innovations
1. 3GPP start date indicates approval of study package (study item->work item->specifications), previous release continues beyond start of next release with functional freezes and ASN.1
New verticals, deployments, use cases, and spectrum
Longer-term evolution to deliver on the 5G vision
Unified, future-proof platform
Rel-15
Rel-171
Rel-161
Rel-191
Rel-20+ evolution
Rel-181
2018
2020
2019
2022
2021
2025
2023
2024
2026
2027+

## Slide 7: 3GPP RAN Rel-18 and Rel-19 Timeline
We are here
R18 RAN1
R18 RAN2/3/4
R18 RAN1 Func. Freeze
R18 RAN2/3/4 Func. Freeze
R18 Maint
R18 Maint
2022
Q1
Q2
Q3
Q4
2023
Q1
Q2
Q3
Q4
2024
Q1
Q2
Q3
Q4
R18 ASN.1 Freeze
2025
Q1
Q2
Q3
Q4
R19 RAN1
R19 RAN2/3/4
R19 RAN1 Func. Freeze
R19 RAN2/3/4 Func. Freeze
R19 ASN.1 Freeze

## Slide 8: RAN Rel-18

## Slide 9: RAN Rel-18 Driving a balanced 5G evolution
Mobile broadband evolution vs. further vertical expansion
Immediate commercial needs vs. longer-term 5G vision
New and enhanced devices vs. network evolution
Deliver enhanced mobile broadband experiences and extend 5G’s reach into new use cases
Drive new value in commercialization efforts and fully realize 5G’s potential with future deployments
Focus on the end-to-end technology evolution of the 5G system to bring new levels of performance
Release 18 takes into consideration of 5G Advanced evolution and beyond (i.e., many Study Items defined to set up for Work Items in later releases)

## Slide 10
The package has a wide range of projects — nominal work started in Q2 2022 with functional freeze in Q4 2023
3GPP Release 18 sets off the 5G Advanced Evolution
Release 18
Strengthen the end-to-end 5G system foundation
Proliferate 5G to virtually all devices and use cases
Advanced DL/UL MIMO
Enhanced mobility
Mobile IAB, smart repeater
AI/ML data-driven designs
Green networks
Evolved duplexing
Boundless extended reality
Expanded sidelink
RedCap evolution
Multicast & other enhancements
Expanded positioning
Drones & expanded satellites comm.

## Slide 11: RAN Rel-19

## Slide 12
RAN1/2/3 package approved in Dec ‘23
RAN4 package approved in Mar ‘24
5G Advanced Release 19 focus areas
3GPP Release 19
Realizing the full potential of 5G
Addressing real and urgent commercial needs
3GPP Release 19
Bridging to 6G
Establishing the technical foundation
Mobile broadband evolution and further vertical expansion
Continue to enhance mobile experiences and extend 5G’s reach into new areas
Immediate and longer-term commercial needs
Drive new value in commercialization efforts and efficiently enable advanced deployments
New and enhanced devices and network evolution
Focus on the end-to-end 5G technology evolution to bring new levels of performance
Revolutionary system innovations
Conduct advanced research to prepare for formal 6G Study Items in Release 20
New spectrum bands and enabling technologies
Study feasibility of new band ranges and types (e.g., upper mid-band in 7-24 GHz)

## Slide 13
New 5G System Capabilities and a Direction for 6G
Topology
SON/MDT
MIMO
Mobility
XR and metaverse
Satellites evolution
Ambient IoT
Duplexing evolution
Higher mid-band spectrum (i.e., 7—16 GHz)
Integrated sensing and communication
Network energy savings
Low-power wakeup receiver
Wireless AI/ML
Release 19

## Slide 14: RAN1-Led Rel-19 Projects: More Details
Projects | SID/WID | Notes
Channel model for 7-24GHz, SI | RP-234018 | Study for the entire release. Validate using measurements channel model in TR38.901 at least for 7-24GHz
Channel model for ISAC, SI | RP-240799 | Study for the entire release, focusing on channel modeling with frequency range 0.5-52.6GHz, to support object detection and/or tracking. Possible scope expansion beyond channel modeling to be checked in 09/24
Ambient IOT, SI | RP-240826 | Study till Dec’24 for possible WI conversion. Harmonized design for backscattered (up to ~1µW) & active transmission (≤ a few hundred µW) Licensed FR1 FDD. Focusing on two topologies: BS directly to tags, and UE as an intermediate node under network control.
NR MIMO Phase 5, WI | RP-240087 | UE initiated/event-driven beam management; CSI support or up to 128 CSI-RS ports; UE reporting enhancements or cohere joint-transmission under non-ideal sync and backhaul; non-coherent UL codebook for 3Tx; enhanced asymmetric TRP operations
NR duplex operation Evo, WI | RP-240789 | A continuation from Rel-18 study, now converting to specifications. Subband full-duplex operation at the gNB side, including signalling/resource management, random access enhancements, measurement, and cross-link interference enhancements
AI/ML for NR air interface, WI | RP-240774 | Largest project in Rel-19; a continuation from Rel-18 study, now converting to specifications, including normative work on one-sided general framework, beam management and positioning, while continuing study two-sided modeling, data collection, and testing
Low Power WUS/WUR, WI | RP-240801 | A continuation from Rel-18 study, now converting to specifications, including waveform, low-power sync signal, RRM etc.
Network Energy Savings Enh, WI | RP-240170 | Continuation of Rel-18 enhancements, including on-demand SSB Scell, adapt tx signal/channel, and study of on-demand SIB1 for idle UEs
* Additional new & small project(s) may be approved in September 2024, see RP-232745

## Slide 15: RAN2-Led Rel-19 Projects: More Details
RAN2-led | SID/WID | Notes
AI/ML for Mobility, SI | RP-240082 | New full release study expanding from Rel-18 for AI/ML, focusing on network triggered layer 3 mobility only. AI/ML based RRM measurement and event prediction.
NR Mobility enh Phase 4, WI | RP-240299 | Continuation from earlier release; focusing on further enhancements to layer 1/2 triggered mobility (LTM), including inter-CU LTM, measurement enhancements for LTM, conditional LTM, and related RRM enhancements
XR for NR Phase 3, WI | RP-240791 | Continuation from earlier releases, focusing on study of potential multi-modality within a UE, enhancements related to measurement gap/scheduling restriction, study of uplink scheduling using delay/deadline information, and user plane latency reduction.
NTN for NR Phase 3, WI | RP-240775 | Continuation from earlier releases, focusing on DL coverage enhancements, UL capacity enhancements, regenerative payload, RedCap full-duplex/half-duplex. Including also a spin-off as in RP-240846 (Inter RAT mobility support from E-UTRAN TN to NR-NTN)
NTN for IoT Phase 3, WI | RP-240776 | Continuation from earlier releases, focusing on store & forward, and UL capacity enhancements
Multi-hop Sidelink Relays, WI | N/A | WID to be available soon, focusing on layer 2 U2N Relay. Starting with one additional hop, limited service continuity.
* Additional new & small project(s) may be approved in September 2024, see RP-232745

## Slide 16: RAN3-Led Rel-19 Projects: More Details
RAN3-led | SID/WID | Notes
AI/ML for NG-RAN, SI->WI | RP-240323 | Continuation from previous release; two new use cases – network slicing & coverage and capacity optimizations (COOs). Also Rel-18 leftovers. 6 months study followed by WI
Topological Enh, SI->WI | RP-240319 | New project. 6 months study followed by WI, focusing on wireless access backhaul (WAB) and 5G femto cells
SON/MDT Enh, WI | RP-234038 | Continuation from previous releases; mobility robustness optimization, intra-NTN mobility and network slicing. R18 leftovers
* Additional new & small project(s) may be approved in September 2024, see RP-232745

## Slide 17: RAN4-led Rel-19 Projects: More Details
RAN4-led | SID/WID | Notes
UE RF enhancements, WI | RP-240828 | Higher UE Tx power for CA, power reduction (MPR/A-MPR) reduction enhancements, 6Rx requirements
Base Station RF enhancements, WI | RP-240829 | EIRP mask definition for 6GHz based on ITU definition and OTA test reduction
NTN enhancements, WI | RP-240857 | Higher UE power classes, enhanced channel models with varying Dopplers for testing, 3MHz channel bandwidth for NTN FR1 bands
RRM enhancements, WI | RP-240830 | Measurement delay reduction for FR2 for CA and UEs capable of multi-Rx, faster SCell activation with early measurement report
Demod enhancements, WI | RP-240831 | 8Rx enhancements with MMSE-IRC and Base Station demod requirements with MMSE IRC
OTA enhancements, WI | RP-240841 | Test methodology for head-worn XR devices, test methodology for FR1 NTN, MIMO OTA with dynamic channel for FR1, TRP/TRS and MIMO OTA requirements for more bands
OTA enhancements, SI | RP-240856 | Test methodology for FR2 UE simultaneous Tx on multiple panels (STxMP); check in 09/24 for potentially new FR2 test methodology for AI/ML
Sidelink, WI | RP-240849 | Contiguous and non-contiguous CA in n48, PC2
Non-Collocated CA/DC, WI | RP-240838 | Requirements for non-collocated deployments with 4 layer MIMO
<5MHz for TN, WI | RP-240832 | Inter-band CA for 3MHz channel BW
ATG enhancements, WI | RP-240839 | CA for ATG (intra-band and inter-band), 2Tx UL MIMO
Study on IMT parameters | RP-240787 | Triggered by ITU WP5D request, IMT parameters for 4400-4800 MHz, 7125-8400 MHz and 14.8-15.35 GHz
Spatial channel model study | N/A | Study new channel models with a spatial component to be used for demod tests, see RP-240792. SID available soon
Study on Fragmented Spectrum/Carriers | N/A | Study ways to reduce the number of Rx chains used to aggregate non-contiguous CCs in a single band (aggregated BW<100MHz), see RP-240768. SID available soon.
* New spectrum items are to be discussed/approved in June 2024. Additional new & small non-spectrum project(s) may be approved in December 2024, see RP-240019

## Slide 18
Initial
6G
Discussion
Continued evolution towards 6G

## Slide 19
Global Momentum for 6G is Growing
United States
NextG Alliance
European Union
6G-IA (6G Smart Networks and Services Industry Association)
China
IMT-2030 PG
Japan
Beyond 5G PC
India
Bharat 6G Alliance
South Korea
6G Forum
IMT-2030 defines next-gen mobile system requirements for 2030 and beyond
The standards body responsible for global 6G technology standardization

## Slide 20: 6G Discussion in 3GPP
3GPP is expected to develop an input to the IMT-2030 process
Initial 6G discussion in 3GPP RAN
  First (very brief) 6G timeline discussion in RAN#101 (September 2023)
    Triggered by the liaison from ITU-R WP5D in RP-231518: On completion of draft new Recommendation ITU-R M.[IMT.FRAMEWORK FOR 2030 AND BEYOND]
  High-level considerations for 6G timeline discussed in RAN#102 (December 2023), including a TSG-wide joint session, resulting in the endorsed way forward in RP-233985
  Additional considerations for 6G timeline discussed in RAN#103 (March 2024), including another TSG-wide joint session, resulting in the endorsed way forward in RP-240823
…

## Slide 21: 6G Timeline Considerations: RAN-Specifics 1/2 (As in RP-233985 and RP-240823)
…
First 3GPP TSG-wide 6G workshop: March 10th – 11th(Monday – Tuesday), 2025
  Right before the planned Rel-19 RAN1 functional freeze (June 2025).
  Details TBD (e.g., whether to have a joint or separate workshop across TSGs, how to handle contributions, etc.)
  TSG#107 plenary meetings are to be scheduled subsequently in the same week
Studies for 6G in 3GPP: from Release 20
RAN plenary work is split into an ITU focused SI (study item) and General RAN SI
  IMT-2030 discussion is expected in RAN from 09/24 to 12/24
  RP SI Rel-20 focusing on ITU– IMT-2030: approval 12/24 until 06/25
  RP SI Rel-20 focusing on 6G General (e.g., radio requirements and KPIs) : approval 03/25 (after WS), until 06/26

## Slide 22: 6G Timeline Considerations: RAN-Specifics 2/2 (As in RP-233985 and RP-240823)
…
RAN WGs in Rel-20
  For 5G-Advanced: 18-month. Assuming no delay of Rel-19
    Stage-1 freeze : Jun 2025
    Stage-2 freeze : Jun 2026 (>=80%); Sep 2026 (100%)
    Stage-3 freeze : Mar 2027
    ASN.1/OpenAPI freeze: June 2027
  For 6G SI: 21 months
    RAN1 starts in 3Q/25 until 1Q/27
    RAN2/3/4 start in 4Q/25 until 2Q/27
IMT-2030 submission and normative work for 6G in 3GPP are expected to start from Release 21
  Release 21 is expected to produce the 1st set of 3GPP 6G technical specifications, and will be the release for IMT-2030 submission before 2030
  Release 21 is expected to be delivered with a single drop (i.e., a single code freeze)
  Rel-21 timeline is to be decided no later than June 2026
    However, ASN.1/OpenAPI freeze date is no earlier than March 2029

## Slide 23
2024
#103
Mar.
#111
Mar.
#107
Mar.
#104
Jun.
#108
Jun.
#112
Jun.
#105
Sep.
#109
Sep.
#102
Dec.
#106
Dec.
#110
Dec.
Now
TSGs
Workshop 6G TSGs
#113
Sep.
#114
Dec.
#115
Mar.
Jun
RAN1
RAN Completion (RAN2/3/4core)
#116
RAN4 Perf
RP IMT-2030 disc.
RP ITU Study
RP 6G Study(ies)
RAN1 6G Study(ies)
5G-Advanced
6G Study
2025
2026
2027
RAN2/3/4 6G Study(ies)
Illustration of 3GPP RAN Rel-20 Timeline

## Slide 24: 3GPP SA Rel-19 status Update and 6G Planning
Puneet Jain
3GPP SA Plenary Chair
Sr. Principal Engineer & Sr. Director, Intel Corporation
April 3, 2024

## Slide 25: 3GPP Rel-18 and Rel-19 Timeline

## Slide 26: Rel-19 Target Dates (Unchanged)
Key target dates for Rel-19
  Stage-1 target freeze: Dec 2023 (Stage-1 has been frozen)
  Stage-2 target freeze: Dec 2024
  Stage-3 target freeze: Sep 2025
  ASN.1/Code target freeze: Dec 2025

## Slide 27: SA Rel-19 Content Definition Process

## Slide 28: SA Rel-19 Content Planning (Step 1)

## Slide 29
SA Rel-19 Content Planning (Step 2)
Tdoc# | Rel-19 Study Title | Rapporteur(s)/ Comment
SP-231805 | Study on Architecture enhancement for XRM Ph2 | Nokia, Meta
SP-231391 | Study on 5GS Enhancement for Energy Efficiency and Energy Saving as Service Criteria | Samsung, Lenovo
SP-231196 | Study on system architecture for next generation real time communication services Ph 2 | China Mobile
SP-231199 | Study on Integration of satellite components in the 5G architecture Phase III | THALES, CATT
SP-231672 | Study on MPS for IMS Messaging and SMS services* | Peraton Labs
SP-231795 | Study on UPF enhancement for Exposure and SBA Phase 2 | ZTE, Vodafone
SP-231796 | Study on Enhancement of support for Edge Computing in 5G Core network phase 3 | Intel
SP-231797 | Study on architecture aspects of 5G Femto | NTT DOCOMO
SP-231798 | Study on System Enhancement for Proximity-based Services in 5GS - Phase 3 | AT&T, KPN
SP-231799 | Study on Architecture Enhancements for Vehicle Mounted Relays (VMR) Phase 2 | Qualcomm, Sony
SP-231800 | Study on Core Network Enhanced Support for AI/ML | vivo, MediaTek
SP-231801 | Study on Phase 3 for UAS, UAV and UAM | LG Electronics, Ericsson
SP-231802 | Study on Multi-Access (Dual 3GPP access + ATSSS Enhancements) | Apple, China Telecom
SP-231803 | Study on Architecture support of Ambient power-enabled Internet of Things | Huawei, OPPO Only Study. Check in Dec 2024
SP-231804 | Study on the Enhancement of Usage of User Identifiers in the 5G System | InterDigital, Inc.
SP-231754 | Study on Architecture Enhancement to support Integrated Sensing and Communication | No study. Check in Sep 2024
SP-231052 | Network Sharing Enhancements SA WG2 Status | Possible TEI19
SP-231503 | New WID on Architecture support of Roaming Value Added Services | Possible TEI19
SP-231674 | Study on Improvements of network controlled Network Slicing Selection | Possible TEI19
SP-231757 | Study on enhancement of Timing Resiliency, TSC&URLLC and LAN | Noted
SP-231701 | Study on Enhanced Traffic Management | Noted
SP-231682 | New WID on Study on Sidelink time synchronisation | Noted
After lengthy online and offline discussions, the SA Chair prepared a proposal (in SP-231760) on Rel-19 content, reflecting a balance of Rel-19 priority from the Operators and Vendors side, which was endorsed
Based on SP-231760, SA#102 approved a package of 15 study items (green in the table)
  AI/ML study: whether SA2 can start work on Work Tasks 1.1, 1.2, and 1.3 will be discussed at SA#105 (Sep. 2024) based on the outcome of the related work in the involved RAN WGs
  Ambient IoT: check in TSG#106 (Dec’24) for further Ambient IoT work taking into account RAN Ambient IoT progress
The Sensing study (cyan in the table) was only endorsed. The work on this study is postponed until Sep 2024 when it will be determined if/when to start the study
Three study item proposals (yellow in the table) will be considered as a small technical enhancement (TEI19)
The remaining items (red in the table) were not considered as part of Rel-19 content
Source: SP-231760

## Slide 30: SA1 Release 19 SIDs/WIDs
Name | Acronym | %Complete | Hyperlink | Impacted TSs and TRs
Study on Energy Efficiency as service criteria | FS_EnergyServ | 100% | SP-230235 | 22.882
Stage 1 of Energy Efficiency as Service Criteria | EnergyServ | 100% | SP-230520 | 22.261
Study on AI/ML Model Transfer Phase2 | FS_AIML_MT_Ph2 | 100% | SP-220439 | 22.875; 22.876
AI/ML Model Transfer Phase 2 | AIML_MT_Ph2 | 100% | SP-230514 | 22.261
Study on Ambient power-enabled Internet of Things | FS_AmbientIoT | 100% | SP-220085 | 22.84
Stage 1 of Ambient power-enabled Internet of Things | AmbientIoT | 95% | SP-231403 | 22.261
Study on satellite access - Phase 3 | FS_5GSAT_Ph3 | 100% | SP-220679 | 
Stage 1 of Satellite access Phase 3 | 5GSAT_Ph3 | 100% | SP-230516 | 22.261
Study on Localized Mobile Metaverse Services | FS_Metaverse | 100% | SP-220353 | 22.856
Stage 1 of Localized Mobile Metaverse Services | Metaverse | 100% | SP-230509 | new 22.156, 22.261 ; 22.156
Supporting UE Mobility for XR Services | XRMobility | 100% | SP-230233 | 22.261
Study on Integrated Sensing and Communication | FS_Sensing | 100% | SP-220717 | 22.837
Stage 1 of Integrated Sensing and Communication | Sensing | 100% | SP-230750 | 22.137
Study on (Stage 1 of) UAV Phase 3 | FS_UAV_Ph3 | 100% | SP-220954 | 
Stage 1 of Uncrewed Aerial System Phase 3 | UAS_Ph3 | 100% | SP-230518 | 
Study on Network Sharing Aspects | FS_NetShare | 100% | SP-220087 | 22.851
Indirect Network Sharing | NetShare | 100% | SP-230511 | 22.261
Study on Upper layer traffic steering, switching and split over dual 3GPP access | FS_DualSteer | 100% | SP-220445 | 22.841
Upper layer traffic steering and switching over dual 3GPP access | DualSteer | 95% | SP-231412 | 22.261
Edge Computing Considering the Operational Needs of Service Hosting Environment | EdgeOpNeeds | 100% | SP-231037 | 22.261
Study on FRMCS Phase 5 | FS_FRMCS_Ph5 | 100% | SP-220437 | 22.989
FRMCS Phase 5 | FRMCS_Ph5 | 100% | SP-230512 | 22.280; 22.179; 22.289; 22.261
Study on Supporting of Railway Smart Station Services | FS_RAILSS | 100% | SP-190838 | New ; 22.890
Study on Network of Service Robots with Ambient Intelligence | FS_SOBOT | 100% | SP-220447 | 22.916
Study on roaming value added services | FS_RVAS | 100% | SP-220442 | 22.877
Roaming Value-Added Services | RVAS | 100% | SP-230231 | 22.261
Study on Interconnect of SNPN | FS_ISN | 65% | SP-230236 | 22.848
Interconnect of SNPN | ISN | 100% | SP-240194 | 
Edge Computing for Industrial Scenarios | EDGINDUS | 100% | SP-230229 | 22.104
PS Data Off for IMS Data Channel Service | IMSDCDataOff | 100% | SP-230227 | 22.011
Multi-path relay | MultiRelay | 100% | SP-220943 | 22.261
UE-to-UE multi-hop relay | UEMHopRelay | 100% | SP-230521 | 22.261; 22.280
Interworking of Non-3GPP Digital Terrestrial Broadcast Networks with 5GS Multicast Broadcast Services | DTT4MBS | 100% | SP-220941 | 22.261
MPS for Messaging services | MPS4msg | 100% | SP-220939 | 22.153
Minimization of Service Interruption During Core Network Failure Phase 2 | MINT_Ph2 | 100% | SP-220992 | 22.261
Measurement Data Collection | MeasureData | 100% | SP-221263 | 22.261
Local traffic routing for multi-access UE | LTR_MA | 100% | SP-231035 | 22.261
Non-Public Network (NPN) security considerations | SecNPN | 100% | SP-230523 | 22.261

## Slide 31: SA2 Release 19 SIDs
Name | Acronym | %Complete | Hyperlink | Impacted TSs and TRs
Study on Energy Efficiency and Energy Saving | FS_EnergySys | 55% | SP-231391 | 23.700-66
Study on Core Network Enhanced Support for Artificial Intelligence (AI)/Machine Learning (ML) | FS_AIML_CN | 25% | SP-231800 | 23.700-84
Study on Architecture support of Ambient power-enabled Internet of Things | FS_AmbientIoT | 25% | SP-231803 | 23.700-13
Study on Integration of satellite components in the 5G architecture Phase 3 | FS_5GSAT_Ph3_ARCH | 55% | SP-231199 | 23.700-29
Study on Extended Reality and Media service (XRM) Phase 2 | FS_XRM_Ph2 | 45% | SP-231671 | 23.700-70
Study on (Stage 2 of) Phase 3 for UAS, UAV and UAM | FS_UAS_Ph3 | 50% | SP-231801 | 23.700-59
Study on Multi-Access (DualSteer and ATSSS_Ph4) | FS_MASSS | 30% | SP-231802 | 23.700-54
Study on Enhancement of support for Edge Computing in 5G Core network - Phase 3 | FS_eEDGE_5GC_Ph3 | 50% | SP-231796 | 23.700-49
Study on System aspects of 5G NR Femto | FS_5G_Femto | 40% | SP-231797 | 23.700-45
Study on Proximity-based Services in 5GS Phase 3 | FS_5G_ProSe_Ph3 | 45% | SP-231798 | 23.700-03
Study on Vehicle Mounted Relays Phase 2 | FS_VMR_Ph2 | 40% | SP-231799 | 23.700-06
Study on User Identities and Authentication Architecture | FS_UIA_ARC | 35% | SP-231804 | 23.700-32
Study on UPF enhancement for Exposure And SBA Phase 2 | FS_UPEAS_Ph2 | 45% | SP-231795 | 23.700-54
Study on system architecture for next generation real time communication services phase 2 | FS_NG_RTC_Ph2 | 45% | SP-231196 | 23.700-77
Study on MPS for IMS Messaging and SMS services | FS_MPS4msg | 70% | SP-231197 | 23.700-75

## Slide 32: SA2 Release 19 Normative TEI19 miniWIDs
Name | Acronym | %Complete | Hyperlink
(Stage 2 of) Indirect Network Sharing | TEI19_NetShare | 0% | SP-240117
Architecture support of roaming value-added services | TEI19_RVAS | 0% | SP-240119
ProSe support in NPN | TEI19_ProSe_NPN | 0% | SP-240122
5GS enhancement on On-demand broadcast of GNSS assistance data | TEI19_OBGAD | 0% | SP-240116
Minimize the Number of Policy Associations | TEI19_MINPA | 0% | SP-240118
Spending Limits for UE Policies in Roaming scenario | TEI19_SLUPiR | 0% | SP-240120
Enhancing Parameter Provisioning with static UE IP address and UP security policy | TEI19_IP_SP_EXP | 0% | SP-240121
Multiple Location Procedure for Emergency LCS Routing | TEI19_MLR4RTR | 0% | SP-240123
Roaming traffic offloading via session breakout in HPLMN | TEI19_HSBO | 0% | SP-240124
Deferred 5GC-MT-LR Procedure for Periodic Location Events based NRPPa Periodic Measurement Reports | TEI19_DLPMR | 0% | SP-240125
5GS enhancement on QoS monitoring enhancement | TEI19_QME | 0% | SP-240126
Subscription control for reference time distribution in EPS | TEI19_TIME_SUB_EPS | 0% | SP-240127
Providing per-subscriber VLAN instructions from UDM and DN-AAA | TEI19_VLANSUB | 0% | SP-240128
NF discovery and selection by target PLMN | TEI19_TPlmnNfSel | 0% | SP-240129

## Slide 33: SA3 Release 19 SIDs/WIDs
Name | Acronym | %Complete | Hyperlink | Impacted TSs and TRs
Study on Security Aspects of 5G Satellite Access Phase 3 | FS_5GSAT_Ph3_SEC | 10% | SP-231790 | 33.700-29
5G Security Assurance Specification (SCAS) for the Unified Data Repository (UDR) | SCAS_5G_UDR | 10% | SP-230864 | 33.926
5G Security Assurance Specification (SCAS) for the Short Message Service Function (SMSF) | SCAS_5G_SMSF | 40% | SP-231158 | 33.529
Addition of 256-bit security Algorithms | 256_Algo | 100% | SP-231159 | 35.248; 35.247; 35.246; 35.245; 35.244; …
Addition of Milenage-256 algorithm | Milenage_256 | 5% | SP-231792 | 35.237; 35.236; 35.235; 35.234
Study on enabling a cryptographic algorithm transition to 256-bits | FS_CAT256 | 10% | SP-231788 | 33.700-41
Study on enablers for Zero Trust Security | FS_eZTS | 20% | SP-231784 | 33.794
Mission critical security enhancements for release 19 | MCXSec4 | 0% | SP-231783 | 33.18
Study on the security support for the Next Generation Real Time Communication services phase 2 | FS_NG_RTC_SEC_Ph2 | 0% | SP-231785 | 33.79
Study on security for PLMN hosting a NPN | PLMNNPN_SEC | 25% | SP-231786 | 33.757
Study of ACME for Automated Certificate Management in SBA | FS_ACME_SBA | 0% | SP-231787 | 33.776
3GPP profiles for cryptographic algorithms and security protocols | CryptoSP | 0% | SP-231793 | 33.127; 33.203; 33.210; 33.222; 33.246; …
Study on mitigations against bidding down attacks | FS_MiBiDA | 0% | SP-231789 | 33.701
Security for mobility over non-3GPP access to avoid full primary authentication | FS_Non3GPPMob_Sec | 0% | SP-231791 | 33.702
Study on security aspects of energy saving in 5G | FS_EE_5G_SEC | 0% | SP-240512 | 
Study on security aspects of Core Network Enhanced Support for AIML | FS_AIML_SEC | 0% | SP-240509 | 
Study on Security Aspect of Ambient IoT Services in 5G | FS_AIOT_Sec | 0% | SP-240506 | 
Study on security aspects of 5G Mobile Metaverse services | FS_Metaverse_Sec | 0% | SP-240508 | 
Study on UAS security enhancements | FS_UAS3_Sec | 0% | SP-240504 | 
Study on security aspects for Multi-Access (DualSteer + ATSSS Ph-4) | FS_MASSS_Sec | 0% | SP-240511 | 
Study on Security Aspects of Enhancement of Support for Edge Computing in 5GC phase 3 | FS_EDGE_Ph3 | 0% | SP-240510 | 
Study on security aspects of 5G NR Femto Document for: Approval | FS_5G_Femto_Sec | 0% | SP-240505 | 
Study on Security Aspects of Enhancement for Proximity Based Services in 5GS Phase 3 | FS_5G_ProSe_Ph3_SEC | 0% | SP-240513 | 
Study on security aspects of User Identities and Authentication | FS_UIA_Sec | 0% | SP-240507 | 
Security aspects for MSGin5G Service Phase 3 | 5GMARCH_SEC_Ph3 | 0% | SP-240516 | 33.501
Security Assurance Specification for maintenance of 5G features | SCAS_5G_Maint | 0% | SP-240515 | 

## Slide 34: SA4 Release 19 SIDs/WIDs

## Slide 35: SA5 Release 19 SIDs/WIDs
Name | Acronym | %Complete | Hyperlink | Impacted TSs and TRs
Study on energy efficiency and energy saving aspects of 5G networks and services | FS_Energy_OAM_Ph3 | 10% | SP-231723 | 28.866
Study on AI/ML management - phase 2 | FS_AIML_MGT_Ph2 | 0% | SP-231780 | 
Study on intent driven management services for mobile network phase 3 | FS_IDMS_MN_Ph3 | 0% | SP-231737 | 
Study on closed control loop management | FS_CCLM | 0% | SP-231735 | 
Study on Cloud Aspects of Management and Orchestration | FS_Cloud_OAM | 0% | SP-231781 | 
Study on Service Based Management Architecture enhancement phase 3 | FS_SBMA_Ph3 | 0% | SP-231725 | 
Study on data management regarding subscriptions and reporting | FS_Data_SREP | 0% | SP-231732 | 
Study on Management Aspects of NTN Phase 2 | FS_NTN_OAM_Ph2 | 0% | SP-231733 | 
Study on management of IAB nodes | FS_NR_mobile_IAB_OAM | 0% | SP-231729 | 
Study on Management of Network Sharing Phase3 | FS_NetShare_OAM_Ph3 | 0% | SP-231731 | 
Study on Enablers for Security Monitoring | FS_SECM | 0% | SP-231736 | 28.87
Study on management aspects of RedCap feature | FS_NR_RedCap_OAM | 0% | SP-231734 | 
Study on management aspects of Network Digital Twin | FS_NDT | 0% | SP-231428 | 28.915
Study on Management Data Analytics (MDA) Phase 3 | FS_eMDAS_Ph3 | 0% | SP-231726 | 
Study on Enhancement of Management Aspects related to NWDAF Phase 2 | FS_NWDAF_OAM_Ph2 | 0% | SP-231724 | 
Study on Management of planned configurations | FS_PlanM | 0% | SP-231721 | 28.872
Study on Enhanced OAM for management exposure to external consumers | FS_MExpo | 0% | SP-231728 | 
Data management phase 2 | MADCOL_Ph2 | 0% | SP-231746 | 28.622; 28.623
5G performance measurements and KPIs phase 4 | PM_KPI_5G_Ph4 | 0% | SP-231747 | 28.552; 32.425; 28.554; 28.532; 28.550; 28.abc
5G Advanced NRM features phase 3 | AdNRM_Ph3 | 0% | SP-231745 | 28.540; 28.541; 28.622; 28.623
Subscriber and Equipment Trace and QoE collection management | TraceQoE_OAM | 0% | SP-231748 | 32.421; 32.422; 32.423; 28.404; 28.405; 28.406; 28.622; 28.623

## Slide 36: SA6 Release 19 SIDS/WIDs
Name | Acronym | %Complete | Hyperlink | Impacted TSs and TRs
Study on application layer support for AI/ML services | FS_AIMLAPP | 55% | SP-231182 | 23.700-82
Study on application enablement for Satellite access enabled 5G Services | FS_5GSAT_Ph3_App | 25% | SP-240296 | 23.700-01
Study on application enablement for Localized Mobile Metaverse Services | FS_Metaverse_App | 30% | SP-231806 | 23.700-21
Study on Application enabler for XR Services | FS_XRApp | 20% | SP-2315739 | 23.700-23
Study on Sensing application enabler for vertical applications | FS_SensingAPP | 0% | SP-231579 | 
Application Architecture for UAS applications Phase 3 | UASAPP_Ph3 | 40% | SP-230991 | 23.255; 23.434
Study on Service aspects for supporting the eMMTel service | FS_eMMTelAPP | 35% | SP-230779 | 23.222 ; 23.700-92
Study on enhanced application layer support for location services | FS_eLSAPP | 40% | SP-240295 | 23.434 ; 23.700-72
Sharing of administrative configuration between interconnected MC service systems | MCShAC | 90% | SP-230692 | 23.280; 23.379; 23.281; 23.282
5GMSG Service phase 3 | 5GMARCH_Ph3 | 35% | SP-230781 | 
Railways specific Enhancements to Mission Critical Services | enh4FRMCS | 40% | SP-230780 | 23.280; 23.281; 23.282; 23.379; 23.283; 23.289
Enhanced Mission Critical Architecture | enhMC | 40% | SP-230988 | 23.280; 23.379; 23.281; 23.282; 23.283; 23.289
SEAL DD (Data Delivery) Phase 2 | SEALDD_Ph2 | 35% | SP-230989 | 
Architecture for enabling Edge Applications Phase 3 | EDGEAPP_Ph3 | 35% | SP-231160 | 23.558
Guidelines for CAPIF Usage | CAPIF_EXT | 55% | SP-231161 | 23.946
Study on CAPIF Phase 3 | FS_CAPIF_Ph3 | 20% | SP-231741 | 23.700-22

## Slide 37: 6G Timeline – Summary
Background
ITU-R has agreed on the timeline for IMT-2030
In Dec ‘23, 3GPP agreed on some first key aspects of the 6G timeline (SP-231693)
3GPP is expected to discuss further details of the 6G timeline in future meetings
Key agreements from SA #102/#103
May ‘24 – 3GPP Stage-1 workshop on IMT-2030 use cases
March ‘25 – 3GPP wide workshop to kick off Rel-20 technical studies in SA and RAN
June ‘25 - Approval of SA2 studies on 6G
6G Studies in Release 20 and 6G normative work in Release 21
Release 21 is expected to be delivered with a single drop (i.e., a single code freeze)
In Mar ‘24, 3GPP agreed on some additional consideration for 6G timeline (SP-240458)

## Slide 38
Stage-1 Workshop on IMT2030 Use Cases: May 8th – 10th (Wednesday – Friday), 2024
First 3GPP TSG-wide 6G Workshop: March 10th – 11th (Monday – Tuesday), 2025
Details TBD (e.g., whether to have a joint or separate workshop across TSGs, how to handle contributions, etc.)
TSG#107 plenary meetings are to be scheduled subsequently in the same week
Studies for 6G in 3GPP: from Release 20
See Next Slide for more details
Normative Work for 6G in 3GPP: from Release 21
Release 21 is expected to produce the 1st set of 3GPP 6G technical specifications, and will be the release for IMT-2030 submission before 2030
Release 21 is expected to be delivered with a single drop (i.e., a single code freeze)
Rel-21 timeline is to be decided no later than June 2026. However, ASN.1/OpenAPI freeze date is no earlier than March 2029
6G timeline – Planning (1/2)

## Slide 39
Rel-20 (5G-Advanced)
  For 5G-Advanced: 18-month. Assuming no delay of Rel-19
    Stage-1 freeze : Jun 2025
    Stage-2 freeze : Jun 2026 (>=80%); Sep 2026 (100%)
    Stage-3 freeze : Mar 2027
    ASN.1/OpenAPI freeze: June 2027
Rel-20 (6G Study Item)
  6G SI Approval
    Other SA WG (SA3, SA4, SA5, SA6) SI approval: TBD at future TSG meeting
    SA1/SA2 6G SI may continue beyond Stage-1/Stage-2 freeze dates for 5G-Advanced
  6G SI Completion (this may use time from Rel-21)
    SA1 6G SI completion: Mar 2026
    SA2 6G SI completion: Dec 2026 or Mar 2027 (To be confirmed at future TSG meeting)
    SA2 SI approval: TSG#108 (Jun 2025)
    SA1 SI approval: TSG#105 (Sept 2024)
6G timeline – Planning (2/2)

## Slide 40
2024
#103
Mar.
#111
Mar.
#107
Mar.
#104
Jun.
#108
Jun.
#112
Jun.
#105
Sep.
#109
Sep.
#102
Dec.
#106
Dec.
#110
Dec.
Now
TSGs
SA1 5GA SID definition
Workshop 6G TSGs
100%
SA1 5GA Studies + Norm 80%
100%
St. 2 (SA2, SA6, …) 5GA SI+ WI 80%
Stage 3 5GA SI + WI
Stage 3 6G SID def.
#113
Sep.
#114
Dec.
#115
Mar.
Jun
Stage-1 Workshop IMT-2030 use cases
#116
SA1 6G Study(ies)
SA1 6G SID def.
SA2 6G Study(ies)
Stage 3 6G Study(ies)
5G-Advanced
6G Study
2025
2026
2027
SA2 6G SID def.
SA3/4/5/6 SID def. TBD
ASN.1 & Open APIs
Illustration of 3GPP SA Rel-20 Timeline
or
TBD
Stage 3 SID def.
Stage 2 SID def.

## Slide 41: 3GPP Stage 1 Workshop on IMT 2030 Use Cases
3GPP Stage 1 Workshop on IMT 2030 Use Cases
(May 8 - 10; Rotterdam, Netherlands)
(For details see - SP-240456)
The objective of the workshop is to bring 3GPP closer to the ongoing initiatives of various global/regional research organizations and MRPs regarding 6G use cases.
This collaborative effort is particularly crucial as SA1 embarks on defining the requirements and use cases for 6G in Rel-20.
Presentations from 3GPP MRPs (e.g. GSMA, 5GAA, …), regional research alliances (Next G Alliance, China IMT 2030 Promotion Group, Japan B5GPC, Kora 6G Forum, Bharat 6G Alliance), and global organizations/institutions (e.g. NGMN, ITU-R).
Conference-style event with a restricted agenda

## Slide 42: Draft Agenda: 3GPP Stage 1 Workshop on IMT 2030 use cases
Note: the order of presentations within the Verticals and within the Research Alliances is subject to change
Time | Wednesday May 8th Opening, Operators, Verticals | Thursday May 9th Research Alliances | Friday May 10th ITU, 3GPP, Closing
1st session | 08.45-09.15: Registration 09.15-09.30: Opening ---------------------------------------------- Operators 09.30-10.00: GSMA 10.00-10.30: NGMN | 09:00-09.45: Japan (B5GPC) 09.45-10.30: South Korea (6G Forum) | 09.00-09.30: ITU-R 09.30-10.00: 3GPP 10.00-10.30: Panel#4: “ITU & 3GPP synergies for 6G”
Morning break | Morning break (10.30-11.00) | Morning break (10.30-11.00) | Morning break (10.30-11.00)
2nd session | 11.00-11.40: Panel#1: “6G Drivers for Operators” ---------------------------------------------- Verticals 11.45-12.10: Automotive (5GAA) 12.10-12.35: Industry (5G-ACIA) | 11.00-11.45: China (IMT2030 Promotion Group) 11.45-12.30: India (Bharat 6G Alliance) | 11.00-11.40: Summary read-out of the Workshop 11.40-12.00: Next steps 12.00-12.30: Closing
Lunch break | Complimentary lunch (12.35-14.00) | Complimentary lunch (12.30-14.00) | Workshop ends 12.30 latest
3rd session | 14.00-14.25: Multimedia (5GMAG) 14.25-14.50: Satellite (GSOA) 14.50-15.15: Public Safety (TCCA) 15.15-15.40: WBA | 14.00-14.45: America (ATIS Next G Alliance) 14.45-15.30: Europe (6G-SNS) | 
Afternoon break | Afternoon break (15.40-16.10) | Afternoon break (15.30-16.00) | 
4th session | 16.10-17.00: Panel#2 : “6G Drivers for Verticals” | 16.00-17.00: Panel#3: “Building a Global 6G View” | 
(Source: SP-240456)

## Slide 43: Questions and Answers
Wanshi Chen Qualcomm 3GPP RAN Plenary Chair
Iain Sharp
ATIS
Puneet Jain Intel Corporation 3GPP SA Plenary Chair
Moderator
Slides and recording will be provided after the event.
3GPP RAN: Current Status and Beyond
3GPP SA Release 19 Status Update and 6G Planning

## Slide 44
Thanks to the speakers and participants